## Slide 1
Water Related Indicators for Sustainable Crop-Livestock Intensification Planning
in Ethiopia: ‘Quick-Water’

## Slide 2
Objective: to provide a tool which can be used to support the spatial targeting of agricultural intensification practices to areas where the biophysical and livelihood conditions are likely to sustain long term development. Water is the entry point.
Project scope and limitations: proof of concept/demonstration of what is possible; short term project with limited time/resources
Team: Economist/policy – Gebre; Crop specialist – Teklu; Livestock – Amare; Water – Charlotte; Spatial – Catherine/Yenenesh/An/Abisalom; Simon
Process: identification of trajectories and indicators; consultation with line agencies at regional/national level; incorporation of feedback in product development
Development of simple tool which produces national maps of selected trajectories and targets

## Slide 3
  Do agricultural intensification initiatives account for water centered issues? (from MERET to AgWATER)
  Is there consistency across different initiatives / policies locally and nationally?
  Are the indicators for agricultural intensification planning strategies based on local and global experience?
  Are ongoing intensification efforts embedded in the livelihood of local communities?
Some key challenges to making intensification sustainable:

## Slide 4: Identifying Development Trajectories for Ethiopia:
Principles
Process

## Slide 5: Description of the selected trajectories
Trajectories | Description
Integrated Natural Resources Conservation based crop- livestock systems intensification | Soil erosion and nutrient depletion is the major focus Crop, livestock and trees are system components with a number of sub trajectories
Small-Scale Irrigation Based Crop-Livestock Intensification | Highly populated area with access to surface or ground water for irrigation with access to market
Large-Scale Irrigation Based Crop-Livestock Intensification | Areas with large irrigable land (>3000 hectares), with high value commercial or industrial crops, where crops and livestock are major components
Agro-Pastoral Rainfed Based Crop-Livestock Intensification | Receives sufficient rainfall, soil is relatively deep and fertile, crop, livestock and trees are major components
Pastoral Livestock Based Intensification | Livestock are the major components where feed, water, veterinary services and market are major issues
Peri-Urban Dairy Based Crop-Livestock Intensification | Dairy, fattening and vegetable farming on small plots are the major components; poultry may also be integrated
Vertisol Management Based Intensification | Water logged vertisol areas receiving high rainfall, especially where temperature is mild to induce high evaporation. Crop and livestock are both major components.
Rainfed commercial farming intensification in crop-livestock systems | Extensive arable land sparsely populated and receiving sufficient rainfall, where commercial/high value and industrial crops are suitable

## Slide 6: Description and reason for selection of indicators / proxies
Trajectory | Indicator / proxy | Simplified reason for selection
Soil & water conservation in crop livestock systems | erosion rate | Major process of land degradation
 | population density | Driver of land use pressure / competition; resource demand
 | livestock density | Driver of land use pressure / competition; resource demand
Small-medium scale irrigation in crop livestock systems | irrigable area OR | Area suitable for irrigation (potential for small/ medium)
 | presence of shallow ground water (15-20m) | Based on geological data
 | protected forest area | Avoid protected forest areas
 | access to market | Necessary for sale of cash crop and access to inputs
Rainfed smallholder intensification in crop-livestock systems or agro-pastoralist systems | minimum annual rainfall | Sufficient rainfall present
 | maximum annual rainfall | Sufficient rainfall present
 | protected forest area | Avoid protected forest areas
 | population density | Driver of land use pressure / competition; resource demand
Large scale irrigation | potential large scale irrigation | Area suitable for large scale irrigation (>3000ha)
 | all-weather roads | Necessary for sale of cash crop and access to inputs
Livestock based intensification | minimum aridity index | Not suitable for crop
 | maximum aridity index | Not suitable for crop
 | population density | Driver of land use pressure / competition; resource demand
 | livestock density | Driver of land use pressure / competition; resource demand
 | Difference: current & potential capacity | Difference between current stocking rate and potential capacity
Peri-urban dairy | access to market OR | Necessary for sale of milk
 | Addis neighbourhood | Largest milk market potential
Vertisol management | Vertisol / soil map | Vertisol area present
 | minimum annual rainfall | Amount of rainfall above which waterlogging occurs
Rainfed commercial farming intensification in crop-livestock /agro-pastoralist systems | minimum annual rainfall | Sufficient rainfall present
 | maximum annual rainfall | Sufficient rainfall present
 | protected forest area | Avoid protected forest areas
 | population density | Driver of land use pressure / competition; resource demand

## Slide 7: Transforming indicators into maps
For each indicator spatial data (geographical layer) is identified
1 indicator = 1 map
=> Mapping tool box

## Slide 8: Mapping toolbox
Combines indicator maps into trajectories
Livelihood scale
  Units of observation are livelihood zones
  Links trajectories to livelihoods
  FEWSNET livelihood zone map (180 zones):
    Areas within which households (on average) share similar livelihood patterns
    i.e. they have access to the same set of food and cash income sources and to the same markets

## Slide 9: The mapping toolbox
Trajectories
Arc GIS
Indicator 1 (I1)
Indicator 2 (I2)
Indicator 3 (I3)
Excel sheet
I1zj> x1
I2zj> x2
I3zj> x3
Suitable livelihood zone for a given intensification trajectory
Spatial processing
Aggregates indicator maps to livelihood maps (by zonal statistic)
Selects livelihood zones where all of conditions of the indicators are met

## Slide 10: Live demonstration of tool

## Slide 11
Soil and water conservation intensification areas

## Slide 12
Small and medium scale irrigation intensification areas

## Slide 13
Areas with potential for multiple combinations of livelihood trajectories